## Slide 1
Giovanna De Chiara
Satellite information on the ocean surface: Scatterometer, Altimeter and SMOS
22 March 2019
with contributions from Saleh Abdalla, Magdalena Balmaseda, Hao Zou, Tony McNally, Patrick Laloyaux, Cristina Lupu, Nicolas Reul (Ifremer)

## Slide 2
Scatterometer Winds
The importance of scatterometer wind observations
Scatterometer principles
Data usage at ECMWF and their impact
How we can improve usage and impact
Altimeter Wind, Waves, Sea Surface Height
Altimeter principles
Use of altimeter data in the wave and ocean models
Altimeter data impacts
SMOS winds
Principles
Database available
TC examples
Outline

## Slide 3
Why is Scatterometer important?
The scatterometer measures the ocean surface winds (ocean wind vector).
Ocean surface winds:
affect the full range of ocean movement
modulate air-sea exchanges of heat, momentum, gases, and particulates
direct impact on human activities
Wind observations below 850 hPa
FSO values relative quantities (in %)
Wide daily coverage of ocean surface winds
[Horanyi et al., 2013]
Ex: 1 day of ASCAT-A data

## Slide 4
A Scatterometer is an active microwave instrument (side-looking radar)
  Day and night acquisition
  Not affected by clouds
The return signal, backscatter (σ0 sigma-nought), is sensitive to:
  Surface wind (ocean)
  Soil moisture (land)
  Ice age (ice)
Scatterometer
Scatterometer was originally designed to measure ocean wind vectors:
  Measurements sensitive to the ocean-surface roughness due to capillary gravity waves generated by local wind conditions (surface stress)
  Observations from different look angles: wind direction
Received
Transmitted

## Slide 5: Scatterometer
The amount of backscatter depends on:
The frequency and polarization of the emitted wave
Backscatter highly depends on:
Incidence angle (largest sensitivity to changes in winds between 30 and 60 deg)
Wind speed
Relative direction between the surface wind and look angle
C-band (5.3 GHz): λ ~ 5.7 cm
Ku-band (13.5 GHz): λ ~ 2.1 cm
Bragg scattering occurs from the ocean capillary-gravity waves (cm-range) that are in resonance with the microwaves

## Slide 6
C- band scatterometers (Fan beam)
Used on European platforms (1991 onwards):
SCAT on ERS-1, ERS-2 by ESA
ASCAT on Metop-A, Metop-B, Metop-C by EUMETSAT
f~5.3 GHz (λ~5.7 cm)
Two sets of three antennas
σ0 on a 12.5 km or 25 km grid
Pros and cons:
Hardly affected by rain
High quality wind direction (especially ASCAT)
Two nearly opposite wind solutions
Rather narrow swath:
ERS-1/2: 500 km
ASCAT-A/B/C: 2x550 km

## Slide 7
Ku-band scatterometers (Rotating pencil beam)
Used on US, Japanese, Indian and Chinese platforms:
NSCAT, QuikSCAT, SeaWinds by NASA (and Japan)
Oceansat, ScatSAT by ISRO
Haiyang-2A/B by China
RapidSCAT on the ISS
Pros and cons:
Up to four wind solutions (rank-1 most often the correct one)
Broad swath (1,800 km)
Affected by rain
Problems regarding wind direction:
  azimuth diversity not good in centre of swath
  outer 200 km only sensed by one beam.
f~13.5 GHz (λ ~ 2.1 cm)
Two rotating pencil-beams (4 look angles)
OSCAT daily coverage

## Slide 8
Dependency of the backscatter on... Wind speed

## Slide 9
upwind
downwind
crosswind
Dependency of the backscatter on... Wind direction
upwind
downwind
Wind direction wrt Beam
  Asymmetry Upwind – Downwind (particularly small)
  Asymmetry Upwind – Crosswind
Using multiple observations from different azimuth angles improves the accuracy of the derived wind direction

## Slide 10
How can we relate backscatter to wind speed and direction?
The relationship is determined empirically
Ideally collocate with surface stress observations
In practice with buoy and 10m model winds
Geophysical model functions (GMF) families
C-band: CMOD (currently CMOD5.N)
Ku-band: NSCAT, QSCAT
U10N: equivalent neutral wind speed
: wind direction w.r.t. beam pointing
: incidence angle
p : radar beam polarization
: microwave wavelength
  Measurements sensitive to the ocean-surface roughness due to capillary gravity waves generated by local wind conditions (surface stress)

## Slide 11
Wind Direction Ambiguity removal
Ambiguities provided
Ambiguities selected
Measurements affected by noise
Each wind vector cell has usually two possible solutions for wind direction and speed.
The correct solution is determined by using NWP forecasts and wind field spatial patterns.

## Slide 12
Operational usage of scatterometer winds at ECMWF
95 | 96 | 97 | 98 | 99 | 00 | 01 | 02 | 03 | 04 | 05 | 06 | 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
ERS-1
ERS-2
ERS-2 (Regional Mission Scenario)
QuikSCAT
METOP-A ASCAT
METOP-B ASCAT
Oceansat-2 (OSCAT)
C-Band
Ku Band
(RapidSCAT)
Passive Monitoring
Coming soon: ASCAT-C (Sep ‘18), CFOSAT (Sep ‘18), Oceansat-3 (Oct ‘18), HY-2B (Nov ‘18)
Reanalysis usage of Scatterometer winds
ERS-2
ERS-2 (Regional Mission Scenario)
ERS-1
QuikSCAT
ASCAT-A
ASCAT-B
Reprocessed

## Slide 13
Scatterometer assimilation strategy
 | C-band | Ku-Band
Resolution | 25 km | 50 km
σ0 bias correction | √ | -
Wind Inversion | ECMWF | KNMI
Wind Speed bias correction | √ | √
QC – Sea Ice check | √ | √
Rain flag check | - | √
Thinning | 100 km | -
Maximum wind speed assimilated | 35 m/s | 25 m/s
Assigned observation error | 1.5 m/s | 2 m/s
4D-Var | 2 solutions | 1 solution
Assimilated as 10m eq. neutral wind (U&V) | √ | √

## Slide 14
TC QC issues
TC KILO – 2015090812 ASCAT-A Observations
ALL
USED
Less observations due to:
Thinning
- VarQC

## Slide 15
Observation weight: VarQC & Huber Norm
Comparing Observation weights:
Gaussian + flat (VarQC): more weight in the middle of the distribution
Huber Norm: more weight on the edges (to data with large departure)
TC QC issues

## Slide 16
TC QC issues
TC KILO – 2015090812 ASCAT-A Observations
ALL
USED
Less observations due to:
Thinning
- VarQC
HN
USED

## Slide 17
Background Departure
ASCAT-A Wind speed O-B
Wind speed bias in the Tropics: also due to Ocean Current?

## Slide 18
Atmospheric wind
Ocean velocity
Atmospheric wind
Ocean velocity
ASCAT sees a calm ocean and underestimates the atmospheric wind speed
ASCAT sees a rough ocean and overestimates the atmospheric wind speed
Scatterometer and Ocean Currents

## Slide 19
Coupled Data Assimilation (CDA)
In the coupled assimilation the SST shows a clear and immediate impact on SST of the storm winds mixing the ocean (cold wake) and the storm’s arrival in the Caribbean damping the usual pronounced diurnal cycle in the SST
In the uncoupled assimilation we rely on external SST from OSTIA. This only shows the impact of the storm winds mixing the ocean some days afterwards (MW/IR) and has no diurnal cycle
Irma/Jose with ocean – atmosphere DA coupling
What about the impact of Scatterometer on the ocean?

## Slide 20
What is the role of ASCAT (and JASON) in the coupled data assimilation during Irma and Jose?
Coupled Data Assimilation (CDA)
In CDA ASCAT gives SST information below Tropical Cyclones
ASCAT sees through the cloud and rain (IR/MW cannot) and informs the coupled analysis of the surface roughening below the storm, in turn influencing the ocean mixing and thus the SST !
Quantifying heat exchange between the storm and ocean surface is an important factor in predicting the intensification / de-intensification of Tropical Cyclones.

## Slide 21
Focus on a specific weather event:
TC Phailin
Bay of Bengal
formed on the 4th October 2013
Argo probe with high-frequency measurements
Temperature measurements at 40-meter depth
Impact of scatterometer surface wind data in the ECMWF coupled assimilation system
P. Laloyaux, J-N Thépaut and D. Dee. MWR, 2016
Impact of scatterometer winds …on the ocean parameters
Coupled Data Assimilation (CDA)

## Slide 22: TC Phailin
Ocean temperature analysis at 40-meter depth (scatterometer data are assimilated)
Coupled analysis with Scatterometer winds is closer to the observations with a stronger cold wake
ASCAT-A
ASCAT-B
OSCAT
Wind measurements from scatterometers (ascending pass, 11 October 2013)
Impact of scatterometer winds …on the ocean parameters

## Slide 23
Impact of Scatterometer on Ocean Temperature
No SCATT – SCATT

## Slide 24
Impact of Scatterometer on Ocean Salinity
No SCATT – SCATT

## Slide 25: Scatterometer Concluding remarks
ECMWF has a long experience with scatterometry
Available continuously from 1991 onwards:
GMF development
Monitoring, validation, assimilation, re-calibration
On-going efforts to improve usage and impact
Improve QC
Adapt observation errors, thinning, super-obbing
Include dependency from other geophysical quantities (i.e. Ocean Currents)
Assessment in coupled system
Use in the Reanalysis
ERS1/2 and QuikSCAT in ERA-Interim
ASCAT-B and ASCAT-A reprocessed products used in ERA5
Scatterometer observations widely used in NWP
Ocean wind vectors
Positive impact on analysis and the forecast
Global scale and extreme events
Impact on Atmospheric, Ocean and Wave model
Typhoon Haiyan 20131107
ASCAT-A ASCAT-B OSCAT

## Slide 26: Radar Altimeters
Radar altimeter is a nadir looking instrument.
Specular reflection.
Electromagnetic wave bands used in altimeters:
Primary:
Ku-band (~ 2.5 cm) – ERS-1/2, Envisat, Jason-1/2/3, Sentinel-3
Ka-band (~ 0.8 cm) – SARAL/AltiKa (only example)
Secondary:
C-band (~ 5.5 cm) – Jason-1/2/3, Topex, Sentinel-3
S-band (~ 9.0 cm) – Envisat
Sentinel-3
Radar Altimeter (SRAL)
Envisat 1-day coverage
Main parameters measured by an altimeter:
  Significant wave height (wave model)
  Wind speed (used for verification)
  Sea surface height (ocean model)

## Slide 27: How Altimeter Works
surface
Height=∆t/2  c
emitted signal returned signal
a t m o s p h e r e
time
ocean surface
illuminated area
Power of illumination
radar signal
time
power
flat surface
rough surface

## Slide 28: Significant Wave Height (SWH)
time
power
waveform
slope of leading edge  SWH
  SWH is the mean height of highest 1/3 of the surface ocean waves
  Higher SWH  smaller slope of waveform leading edge
  Errors are mainly due to waveform retracking (algorithm) and instrument characterisation.

## Slide 29: Surface wind speed
  Backscatter is related to water surface Mean Square Slope (MSS)
  MSS can be related to wind speed
  Stronger wind  higher MSS  smaller backscatter
  Errors are mainly due to algorithm assumptions, waveform retracking (algorithm), unaccounted-for attenuation & backscatter.
amplitude of returned signal  wind speed
time
power
waveform
emitted signal backscatter

## Slide 30: Sea Surface Height
Time delay  sea surface height
  Radar signal attenuation due to the atmosphere is caused by:
    Water vapour impact: ~ 10’s cm.
    Dry air impact: ~ 2.0 m
    Correction made using radiometer and model data
time
power
waveform

## Slide 31: Operational Assimilation of SWH (wave model)
Assimilation method for SWH data:
  Data are subjected to a quality control process (inc. super-obbing).
  Bias correction is applied.
  Simple optimum interpolation (OI) scheme on SWH.
  The SWH analysis increments  wave spectrum adjustments…
10 Mar. 2009
Jason-1 Envisat
Jason-2 Envisat
Envisat
8 Jun. 2009
Jason-1 Jason-2 Envisat
1 Apr. 2010
Jason-2 Envisat
7 Apr. 2012
Jason-2
22 Oct. 2003
ERS-2
1 May 1996
ERS-1
15 Aug. 1993
1 Feb. 2006
12 May 2015
Jason-2 Cryosat-2 SARAL
Jason-3 OGDR (from Q4, 2017); Sentinel-3 (~Q4, 2017).

## Slide 32: All the five altimeter instruments listed below Cryosat-2 (CS2)+ SARAL AltiKa (SA)+ Jason-2 (J2) Sentinel-3A&B Sentinel-3A Sentinel-3Bec. 2018 to 31 Jan. 2019
Altimeter SWH data available from five satellites – nice synergy!
Plot shows random error reduction of SWH compared to model only.
Instrument sinergies

## Slide 33: Impact of one additional altimeter on the SWH analysis [CS & J2] - [J2 only]
Impact of SWH assimilation

## Slide 34
Altimeter data in the Ocean Model
10cm
30 m
From sea level observation it is possible to infer information on the vertical density structure
SLA = Sea Level Anomaly
Assimilated in the ocean model
SLA
The altimeter measures the range which can be used to determine Sea Surface Height (SSH)
SSH

## Slide 35
El Nino 2015/2016
SL Anomalies Feb 2016
Lon/Depth Temp anom Feb 2016

## Slide 36
Sea surface height observations from satellite (i.e. AVISO L3 along track SLA data) are assimilated in ECMWF ocean reanalysis (ORAS4, ORAP5 and ORAS5) system using NEMOVAR.
Satellite data includes observations from ERS-1/2, Envisat, Jason-2/3 and Topex/Poseidon, Altika, HY-2A, Cryosat-2 (Sentinel-3 in the future).
The SLA along track data has very high spatial resolution  Features in the data which the model can not represent.
This can be dealt with in different ways:
  Inflate the observation error to account for non representativeness of the “real” world in the assimilation system
  Construction of “superobs” by averaging
  Thinning
Operational Assimilation of SLA
Obs SLA 10 days
Model (1 deg) SLA in 10 days

## Slide 37
superob
thinning
raw
super-observation is created by averaging SLA value, space/time positions
Thinning is randomly select one observation within each superob-grid
share the same obs number, superob grid and OBE
Operational Assimilation of SLA
Before the assimilation, a thinning or superobbing scheme is normally implemented to avoid over sampling of the satellite observations.

## Slide 38: Impact of assimilating altimeter SLA: Time correlation with altimeter SL product
CNTL
NEMOVAR TS
ORAS4 (TS+Alti)
Impact of SLA assimilation

## Slide 39: Altimeter Concluding remarks
ECMWF has a long experience with altimetry in the wave model
Available continuously from 1993 onwards:
ERS1/2, Envisat, Jason1/2, Cryosat, Saral…
  Now with new missions: Jason-3, Sentinel-3,…
  Altimeter wind and wave data are used for:
  Data assimilation
  Error estimation
  Use in reanalyses (assimilation and validation)
  Long term assessments & climate studies
  Monitoring of model performance (inc. model resolution) & Assessment of model changes
  Altimeter sea level anomaly:
  Use for assimilation and validation
  Significant impact for surface and sub-surface ocean
  Importance for reanalysis and climate studies
  Uncertainty from the ensemble members potentially used for model error

## Slide 40
SMOS
SMOS (Soil Moisture and Ocean Salinity) was launched in November 2009
The SMOS synthetic antenna consists of 69 radiometer elements operating at L-band (frequency ~1.4 GHz, λ=21 cm) and distributed along three equally spaced arms, resulting in a planar Y-shaped structure.
In aperture synthesis radiometers, a TB image is formed through Fourier synthesis from the cross correlations between simultaneous signals obtained from pairs of antenna elements.
Multi-angular images of the brightness temperature are obtained over a large swath width (1200 km), with a spatial resolution varying within the swath from 30 km to about 80 km, and with a revisit time of less than 3 days.

## Slide 41
SMOS wind data
L-band is less affected by rain, spray and atmospheric effects than higher mw frequencies (C-band, Ku-band)
There is no saturation at high wind speed like for radars
Sea foam, generated by breaking waves which mainly depends on surface wind strength and sea state development, increases the microwave ocean emissivity

## Slide 42
Whitecaps
Foam streaks
Ocean-Atmosphere Interface in very High Wind speed conditions
Most of the increased surface whitening at & above hurricane force (>33 m/s) is principally induced by the increased streaks coverage
Whitecap coverage is found ~constant above Hurricane force ~4 [Holthuijsen et al. JGR 2012]

## Slide 43
S.Shen and J. Tenerelli 2007
Rain Anatomy in a hurricane
Rain rate [mm/h]
High winds in Hurricanes are very often associated with High rain rates
Because of the small ratio of raindrop size to the SMOS electromagnetic wavelength (~21 cm), scattering by rain is almost negligible at L-band, even at the high rain rates experienced in hurricanes.

## Slide 44
Increase of the microwave ocean emissivity
with wind speed  surface foam change impacts
This information can be used to retrieve the surface wind speed in Hurricanes:
Principle of the Step Frequency Microwave Radiometer (SFMR)
C-band: => Use multi-frequency C-band channels to separate wind from rain effects
NOAA’s primary airborne sensor for measuring Tropical Cyclone surface
wind speeds since 30 year (Ulhorn et al., 2003, 2007).
Hurricane hunter P-3
Wind speed retrieval in extreme winds : SFMR

## Slide 45
Detect the useful TC & ETC events in SMOS data: Example of EMILIA
SMOS+STORM Evolution
Position of the Storm center at the time of SMOS Aquisition

## Slide 46
Tasks 2: Detect the useful TC & ETC events in SMOS data: Example of EMILIA
SMOS+STORM Evolution

## Slide 47
Tasks 2: Detect the useful TC & ETC events in SMOS data: Example of EMILIA
SMOS+STORM Evolution

## Slide 48
Tasks 2: Detect the useful TC & ETC events in SMOS data: Example of EMILIA
SMOS+STORM Evolution

## Slide 49
Tasks 2: Detect the useful TC & ETC events in SMOS data: Example of EMILIA
SMOS+STORM Evolution

## Slide 50
Tasks 2: Detect the useful TC & ETC events in SMOS data: Example of EMILIA
SMOS+STORM Evolution

## Slide 51
A view at the SMOS-STORM 2010-2015 TC database
Data available at http://www.smosstorm.org/
A subset of 320 SMOS swath intercepts with TCs over 2010-2015, free of Radio Frequency Interferences and with pixel distances >150 km from the coast are selected
https://smos-storm.oceandatalab.com

## Slide 52
Summary
The SMOS brightness temperature signal (∆TB) is clearly associated with the passage of Tropical Cyclones
Correlations between L-band Tb increase with TC intensity from Cat 1 to Cat 5 was demonstrated
L-band observations provide a first non-atmosphere corrupted view of the ocean surface in extreme conditions=> wind speed retrieval with ~5m/s accuracy
A complete storm database as been generated for the SMOS mission archive:
TC & ETC 2010-now available at http://www.smosstorm.org/

## Slide 53
Thanks!!!