## Slide 1: Atmospheric composition

## Slide 2: Data Assimilation of Atmospheric Composition
Antje Inness
Contributions from: Angela Benedetti, Richard Engelen, Johannes Flemming, Sebastien Massart

## Slide 3: Outline
Introduction
Potential benefit for NWP
Challenges for atmospheric composition DA
Observations of atmospheric composition
Aerosol assimilation
Concluding remarks

## Slide 4: 1. Introduction
Environmental and health concern (29,000 premature deaths in UK per year)
Important to provide air quality forecasts
Expertise in data assimilation and atmospheric modelling
Not principally different from meteorological DA but several new challenges
Interaction of atmospheric composition (AC) and NWP
  Feedback on dynamics via radiation scheme
  Precipitation and clouds
  Satellite data observations influenced by aerosols (and trace gases)
  Hydrocarbon (Methane) oxidation is water vapour source
  Assimilation of AC data can have impact on wind field

## Slide 5: Composition-IFS (C-IFS)
Over the last decade IFS has been extended with modules for atmospheric composition (aerosols, reactive gases, greenhouse gases)
GEMS -> MACC -> CAMS (Copernicus Atmosphere Monitoring Service) projects
At first a “Coupled System”, now composition fully integrated into IFS
Data assimilation of AC data to provide best possible IC for subsequent forecasts
AC benefits from online integration and high temporal availability of meteorological fields
C-IFS provides daily analyses and 5-day forecasts of atmospheric composition in NRT

## Slide 6: CAMS Service Provision
Air quality
Global Pollution
Aerosols
Fires
Daily (NRT)
Flux Inversions
Reanalysis
2003 onwards
Ozone records
Retrospective
atmosphere.copernicus.eu
GHG forecast

## Slide 7: CAMS data assimilation system
IFS control variables
CHEM: O3, NO2, SO2, CO, HCHO
AER: single or dual control variables (total or fine & coarse mode aerosol mixing ratio)
GHG: CO2, CH4
Chemistry solvers included in IFS
e.g. TM5 (CB05)
54 species, 126 reactions
photolysis, dry and wet deposition
(no TL + AD of chemistry)
Aerosol model with 12 bins (no TL or AD)
Extra information:
Emissions (e.g. GFAS)
Fluxes
Observations
Observation operators
Varbc
Background error statistics
GHG fields
Meteorological variables

## Slide 8: ECMWF CAMS 4D-VAR Data Assimilation Scheme: Assimilation of AC
transport +
chemistry +
aerosol model
advection only
transport +
chemistry +
aerosol model

## Slide 9: 2. Potential benefit for NWP
Interactive aerosols: Feedback on dynamics via radiation scheme: Tegen AER climatology used in radiation scheme
Use of O3 (& other fields) in the radiation scheme: MACC climatologies used
RTTOV observation operator: Use of O3, CO2 analysis fields to improve the use of radiances sensitive to O3, CO2: model O3 is used, but climatologies used for other tracers (e.g. fixed CO2 value)
Dynamical coupling with wind/ T through TL and AD: turned off
Multivariate JB: Correlations between tracers and dynamical variables, e.g. O3 and vorticity; correlations between chemical species: univariate

## Slide 10: Impact of Aerosol Climatology on NWP
Change in Aerosol Optical Thickness Climatologies
New: Reduction in Saharan sand dust & increased sand dust over Horn of Africa
Old aerosol dominated by Saharan sand dust
26r3: New aerosol (June) Tegen et. al 1997 997):
26r1: Old aerosol (Tanre et al. 84 annually fixed)‏
Thickness at 550nm
J.-J. Morcrette
A. Tompkins

## Slide 11: Surface Sensible heat flux differences
20 W m-2 ~ 20-30%
Boundary layer height increases >1km
old
new
New-old
Impact of Aerosol Climatology on NWP

## Slide 12
Improved forecasts of meridional wind variations at 700 hPa for
the African easterly jet region and
the eastern tropical Atlantic
Improved Predictability with improved Aerosol Climatology
Rodwell and Jung (2008), QJRM., 134, 1479.1497‏
New
Old

## Slide 13: Work in progress: Use of MACC climatology
26r3: New aerosol (June) Tegen et. al 1997 997):
26r1: Old aerosol (Tanre et al. 84 annually fixed)‏
AOD 550nm
J.-J. Morcrette
A. Tompkins
A. Bozzo
MACC
Tegen
Tests are being carried out to use LW and SW aerosol prognostics in radiation code

## Slide 14: Benefit of trace gases for NWP: Variable CO2 in radiance assimilation
Using modelled CO2 in AIRS/IASI radiance assimilation leads to significant reduction in needed bias correction.
Small positive effect on T analysis and neutral scores/ small positive impact at 200 hPa T in Tropics
Stratospheric T in variable CO2 exp more consistent with AMSU-A
It would be beneficial to replace the fixed value by more realistic values
Reduced
AMSU-A
Bias Correction
Reduced AIRS and IASI Bias Correction
Engelen and Bauer, QJRMS, 2011
Fixed CO2
Variable CO2
Mean bias correction (K) for August 2009 for AIRS channel 175 (699.7 cm-1; maximum temperature sensitivity at ~ 200 hPa)
stratosphere

## Slide 15: Wind information from tracers
Prospect to extract wind information from long lived tracers in stratosphere and upper troposphere, e.g. O3, H2O, N2O.
Similar to cloud track winds but data coverage worse
Potential to extract wind info indirectly through TL and AD of tracer advection
Potential was demonstrated in early studies for H2O (Thepaut 1992) and O3 (Daley 1995; Riishojgaard 1996; Holm 1999; Peuch et al. 2000).
Could compliment existing wind observations and help in areas where there is a lack of adequate global wind profile data

## Slide 16: Requirements to extract wind information from tracers
Complete data coverage (3D), frequent observations
Accurate observations
High quality background field
No bias between obs and background
Depends on accuracy of TL model compared to full model (better for passive tracers/ long chemical lifetime) => E.g. extracting wind information from O3 is more difficult in the tropics and summer hemisphere where photochemical lifetime is shorter
Studies have looked at this in idealized experiments (e.g. Daley 1995; Riishojgaard 1996; Peuch et al. 2000; Allen et al. 2013, 2014) focussing on long lived tracers O3, H2O, N2O and found positive impact for perfect observations.
Few studies used real data (e.g. MLS O3, Semane et al. 2009) and positive results are less clear

## Slide 17
Coupling between tracer and wind field in 4D-Var:
illustration using 1D advection model
Tangent linear equations:
Adjoint equations:
Model equations
u = u(x,t) = wind over periodic domain [0,L]
q = q(x,t) = passive tracer
= diffusion coef.
= perturbations
= adjoint variables

## Slide 18
Single observation experiments -
Ozone and wind increments
4D-Var 12z
4D-Var 15z
4D-Var 9z
3D-Var
Level 20,
 30 hPa
6h assimilation window

## Slide 19: Ozone increments at 10S
Associated Temp increments
GOME 15-layer profiles (~15,000 per day)
SBUV 6-layer profiles ( ~1,000 per day)
Impact of ozone data in 4D-Var: Example from ERA-Interim
Large systematic O3 increments
The stratosphere is not well constrained by observations:
Ozone profile data generate large temperature increments
4D-Var adjusts the flow where it is least constrained, to improve the fit to observations
=> IFS O3 analysis is completely uncoupled now
D. Dee
1 hPa
20 hPa

## Slide 20
Benefit of chemical coupling
Background NOx levels determine O3 production/loss
Assimilation of NO2 has an impact on ozone field (through chemical feedbacks in the CTM)
Assimilation of NO2 can improve O3 field
Validation with MOZAIC ozone data
CO & NO2 assim
Control (no CO or NO2 assim, only O3 assim)
MOZAIC observation
NO2 assim

## Slide 21: 3. Challenges for atm. composition data assimilation

## Slide 22: Challenges
Quality of NWP depends predominantly on initial state
AC modelling depends on initial state (lifetime) and surface fluxes
Large part of chemical system not sensitive to initial conditions because of chemical equilibrium, but dependent on model parameters (e.g. emissions, deposition, reaction rates,…)
Data assimilation is challenging for short lived species (e.g. NO2)
CTMs have larger biases than NWP models
Most processes take place in boundary layer, which is not well observed from space
Only a few species (out of 100+) can be observed
Data availability
More complex and expensive, e.g. atmospheric chemistry, aerosol physics
Concentrations vary over several orders of magnitude

## Slide 23: Chemical Lifetime vs. Spatial Scale
◄ into stratosphere
No transport modelled

## Slide 24: Emission Estimates
Emissions are one of the major uncertainties in modeling (can not be measured directly)
The compilation of emissions inventories is a labour-intensive task based on a wide variety of socio-economic and land use data
Some emissions can be “modeled” based on wind (sea salt aerosol) or temperature (biogenic emissions)
Some emissions can be observed indirectly from satellites instruments (Fire radiative power, burnt area, volcanic plumes)
„Inverse“ methods can be used to correct emission estimates using observations and models – in particular for long lived gases such as CO2 (e.g. Chevallier et al. 2014) and Methane (Bergamaschi et al. 2009)
Emissions can be included in the control vector and adjusted together with concentrations (e.g. Hanea et al. 2004; Elbern et al. 2007; Miyazaki et al. 2012)

## Slide 25: Emission Processes
Combustion related (CO, NOx, SO2, VOC, CO2)
  fossil fuel combustion
  biofuel combustion
  vegetation fires (man-made and wild fires)
Fluxes from biogeochemical processes (VOC, CH4, CO2, Pollen):
  biogenic emissions (plants, soils oceans)
  agricultural emissions (incl. fertilisation)
Fluxes from wind blown dust and sea salt (from spray)
Volcanic emissions (ash, SO2, HBr …)
In MACC we use GFAS fire emissions (Kaiser et al. 2012) and MACCity anthropogenic emissions (Granier et al. 2011)
Biomass burning accounts for ~ 30% of total CO and NOx emissions, ~10% CH4

## Slide 26: Importance of emissions (Russian fires 2010)
Assimilation of IASI TCCO leads to improved fit to MOPITT TCCO
TCCO from Assim and Assim-GFAS are very similar
Huijnen et al. 2012 (ACP)
GFAS emissions are needed to get peak in surface concentrations in GFAS and Assim-GFAS
Total column CO
Daily maximum surface O3 and CO

## Slide 27: Importance of fire emissions on tropospheric NO2
GFAS emissions for January used by mistake in IFS-MOZ during 2011

## Slide 28: Impact of anthropogenic emissions: CO Bias - GAW Europa timeseries
C-IFS runs:
HTAP emissions
MACCity emissions
Coupled system:
Reanalysis (MACCity)
(GFAS used in all runs)
J. Flemming
Choice of emissions data set has large impact on surface concentrations

## Slide 29: Short lived memory of NO2 assimilation
OMI NO2 analysis increment [%]
Differences between
[1015 molec/cm2]
JF 2008
JJA 2008
JF 2008
JJA 2008
Large positive increments from OMI NO2 assim
Large differences between analyses of ASSIM and CTRL
Impact is lost during subsequent 12h forecast
It might be more beneficial to adjust emissions (instead of IC)
12h fc from ASSIM and CTRL
Analysis and CTRL

## Slide 30: 4. Observations of atmospheric composition

## Slide 31: Satellite observations
SO2, GOME-2, SACS, BIRA/DLR/EUMETSAT
NO2, OMI, KNMI/NASA
Aerosol Optical Depth, MODIS, NASA
O3, OMI, KNMI/NASA
Atmospheric composition observations traditionally come from UV/VIS measurements. This limits the coverage to day-time only. Infrared/microwave are now adding more and more to this spectrum of observations (MOPITT, AIRS, IASI, MLS, MIPAS …)
CH4, IASI, LMD

## Slide 32: Reactive gases data availability in MACC NRT system: 20140901, 12z
HCHO
GOME-2 Metop-A
OMI
AURA
SO2
GOME-2 Metop-B
GOME-2 Metop-A
OMI
AURA
GOME-2 Metop-A
GOME-2 Metop-B
Tropospheric NO2
IASI Metop-A
IASI Metop-B
MOPITT TERRA
CO
O3
GOME-2 Metop-A
OMI, MLS
AURA
SBUV/2
NOAA-19
monitored
assimilated
GOME-2 Metop-B

## Slide 33: Greenhouse gases data availability in MACC NRT system: 20160224, 0z & 12z
TANSO-FTS
GOSAT
Lower troposphere CH4/CO2
Middle troposphere CH4/CO2
IASI
Metop-A Metop-B
XCH4 in ppb
XCH4 in ppb
OCO-2
20160224, 00Z+12z
20160224, 00Z+12z
XCO2 in ppm
Nadir mode orbit

## Slide 34: Issues with Observations
AC Satellite retrievals
  Little or no vertical information from satellite observations. Total or partial columns retrieved from radiation measurements. Weak or no signal from boundary layer.
  Fixed overpass times and daylight conditions only (UV-VIS) -> no daily maximum/cycle
  Global coverage in a few days (LEO); often limited to cloud free conditions; fixed overpass time.
  Retrieval errors can be large; small scales not resolved
  We use retrievals for AC: Averaging kernels important
AC in-situ observations
  Sparse (in particular profiles)
  Limited or unknown spatial representativeness

## Slide 35
Impact of a single observation in 3D-Var
(for model variable at a gridpoint)
xa: analysis value
xb: background value
y: observation
o2: observation variance
b2: background covariance
B: column of background error covariance matrix
Analysis increment is proportional to a column of B-matrix
B-matrix determines how increment is spread out from a
single observation to neighbouring gridpoints/ levels
Importance of height resolved observations

## Slide 36
Increment created by a single O3 obs
Increment from a single TCO3 observation
Maximum impact around L20 (~35 hPa)
Profile data are important to obtain a good vertical analysis profiles
Horizontal correlations
Standard deviation
Vertical correlations
Ozone background errors
Ozone observation of 247 DU, 66 DU lower than background

## Slide 37
Assimilation (MIPAS)
Control
70S
Ozone hole in GEMS reanalysis: Cross section along 8E over South Pole, 4 Oct 2003
Oct 2004
ASSIM (MIPAS)
CTRL
Assimilation with profile data
Assimilation with total column data

## Slide 38: 5. Aerosol DATA assimilation

## Slide 39: 4D-Var assimilation system for aerosols
Aerosol assimilation is difficult because:
There are numerous unknowns (depending on the aerosol model) and very little observations to constrain them
The concentrations vary hugely with for instance strong plumes of desert dust in areas with very little background aerosol, which makes it difficult to estimate the background error covariance matrix

## Slide 40
The aerosol prediction system: Forward model
12 aerosol-related prognostic variables:
* 3 bins of sea-salt (0.03 – 0.5 – 0.9 – 20 µm)
* 3 bins of dust (0.03 – 0.55 – 0.9 – 20 µm)
* Black carbon (hydrophilic and –phobic)
* Organic carbon (hydrophilic and –phobic)
* SO2 -> SO4
Physical processes include:
emission sources (some updated in NRT, i.e. fires)
horizontal and vertical advection by dynamics
vertical advection by vertical diffusion and convection
aerosol specific parameterizations for
dry deposition, sedimentation, wet deposition by large-scale and convective precipitation, and hygroscopicity (SS, OM, BC, SU)
fine mode
coarse mode

## Slide 41
The aerosol prediction system: Analysis
Assimilated observations are the 550nm MODIS Aerosol Optical Depths (AODs) over land and ocean, and the fine mode AODs over ocean.
Control variable is formulated in terms of the total aerosol mixing ratio.
To come: dual mode control variable. Aerosol control variables are the fine mode (<1 µm diameter) and coarse mode aerosol mixing ratio.
Improvements of dual mode control variable are especially seen in fine mode AOD
Analysis increments are repartitioned into the species according to their fractional contribution to the total or fine/coarse mode aerosol mixing ratio.
Background error statistics were computed using forecasts errors as in the NMC method (48h-24h forecast differences).
Observation errors are prescribed fixed values.
Variational bias corrections are applied to both total and fine mode AOD.
Angela Benedetti

## Slide 42: How does it work?
Nonlinear run:
All bins/species are initialized from a previous forecast; the total aerosol mixing ratio is initialized from sum of all bins/species.
All aerosol variables go through advection, vertical diffusion and convection.
Individual bins/species mixing ratio are used to compute optical depth according to the bin/species-specific optical properties.
Tangent linear/adjoint runs:
Perturbations of optical depth are started from zero perturbations on individual bin/species mixing ratios on the first call of the tangent linear.
These perturbations are then passed to the adjoint routine to compute the gradient wrt individual bin/species mixing ratios. The gradient in the total aerosol mixing is then obtained from
where fi represents the fractional contribution of each bin/species to the total
mixing ratio.
3. The gradient wrt total aerosol mixing ratio is then used in the minimization and
the resulting increment in rt is used in the tangent linear run to compute
updated perturbations on the individual bin/species mixing ratios as follows:
This last step is not fully justifiable unless at all times and at all locations.

## Slide 43
Saharan dust outbreak: 6 March 2004
Model simulation
Assimilation
MODIS
SEVIRI
AERONET
Assimilation
Simulation
March
Cape Verde
Aerosol optical depth at 550nm (upper)
and 670/675nm (lower)

## Slide 44: Example for wrong aerosol attribution
sulphate
biomass
dust
sea salt
The MACC aerosol model did not contain stratospheric aerosol at this time, so the observed AOD was wrongly attributed to the available aerosol types.
MACC AOD analysis
Eruption of the Nabro volcano in June 2011 put a lot of fine ash into the stratosphere.
This was observed by AERONET stations and the MODIS instrument.
AERONET fine mode AOD
ICIPE-Mbita - AERONET
AERONET total AOD

## Slide 45: Why we need profiling data for aerosol assimilation
Graphics by Luke Jones
Aerosol & cloud amounts,
Forecast only
Aerosol & clouds amounts,
AOD Assimilation
CALIPSO feature mask
AOD is a column-integrated quantity
Assimilation of AOD does not modify the vertical profile
Profile data are needed (lidar)
MODIS Aerosol Optical Depth

## Slide 46
NRT CALIPSO level 1.5 product available since mid-2011
Mean Attenuated aerosol backscatter at 532 nm (cloud cleared)
Aimed at operational NWP centres (ECMWF, US Naval Research Lab, JMA,…)
Developed through close collaboration with NASA LaRC CALIPSOTeam
Lidar observation operator in place and performing well
Calipso data have positive impact on the aerosol extinction profile (in initial tests)
(*) Lidar data are courtesy of Arnon Karnieli. Special thanks to
Simone Lolli, Judd Welton and the MPLNET team.
Observations-Model extinction (km-1)
MODIS only
Lidar and MODIS
Observations
Towards lidar assimilation: Impact of Calipso on vertical profiles
Monthly averaged extinction (km-1)
at 532nm at Sede Boker (453 profiles)
Lidar and MODIS
Observations-Model extinction (km-1)
MODIS only

## Slide 47: 6. Concluding remarks
Atmospheric composition (AC) and weather interact
IFS has been extended to include fields of atmospheric composition: Reactive gases, greenhouse gases, aerosols => Composition-IFS (C-IFS)
Modelling of AC needs to include many species with concentrations varying over several orders of magnitude
AC forecasts benefit from realistic initial conditions (data assimilation) but likewise from improved emissions
Extra challenges for DA of atmospheric composition compared to NWP - but also potential benefits through chemical coupling and impact on NWP
CAMS system produces useful AC forecast and analyses, freely available from atmosphere.copernicus.eu

## Slide 48: atmosphere.copernicus.eu
More information about the environmental monitoring activities at ECMWF and how to access the data can be found on:

## Slide 49: References: Reactive Gases
N. Elguindi, H. Clark, C. Ordóñez, V. Thouret, J. Flemming, O. Stein, V. Huijnen, P. Moinat, A. Inness, V.-H. Peuch, A. Stohl, S. Turquety, G. Athier, J.-P. Cammas, and M. Schultz (2010): Current status of the ability of the GEMS/MACC models to reproduce the tropospheric CO vertical distribution as measured by MOZAIC. Geosci. Model Dev., 3, 501-518, 2010
Flemming, J., Huijnen, V., Arteta, J., Bechtold, P., Beljaars, A., Blechschmidt, A.-M., Josse, B., Diamantakis, M., Engelen, R. J., Gaudel, A., Inness, A., Jones, L., Katragkou, E., Marecal, V., Peuch, V.-H., Richter, A., Schultz, M. G., Stein, O., and Tsikerdekis, A.: Tropospheric chemistry in the integrated forecasting system of ECMWF, Geosci. Model Dev. Discuss., 7, 7733-7803, doi:10.5194/gmdd-7-7733-2014, 2014.
Flemming, J., and A. Inness (2013), Volcanic sulfur dioxide plume forecasts based on UV satellite retrievals for the 2011 Grímsvötn and the 2010 Eyjafjallajökull eruption, J. Geophys. Res. Atmos., 118, doi:10.1002/jgrd.50753.
Flemming, J., Inness, A., Jones, L., Eskes, H. J., Huijnen, V., Schultz, M. G., Stein, O., Cariolle, D., Kinnison, D., and Brasseur, G. (2011): Forecasts and assimilation experiments of the Antarctic ozone hole 2008, Atmos. Chem. Phys., 11, 1961-1977, doi:10.5194/acp-11-1961-2011
J. Flemming, Inness, A., Flentje, H., Huijen, V., Moinat, P., Schultz, M.G. and Stein O. (2009): Coupling global chemistry transport models to ECMWF's integrated forecast system. Geosci. Model Dev., 2, 253-265, 2009. www.geosci-model-dev.net/2/253/2009/
Huijnen, V., Flemming, J., Kaiser, J. W., Inness, A., Leitao, J., Heil, A., Eskes, H. J., Schultz, M. G., Benedetti, A., Hadji-Lazaro, J., Dufour, G., and Eremenko, M. (2012). Hindcast experiments of tropospheric composition during the summer 2010 fires over western Russia. Atmos. Chem. Phys., 12:4341–4364.

## Slide 50: References: Reactive Gases
Inness, A., Blechschmidt, A.-M., Bouarar, I., Chabrillat, S., Crepulja, M., Engelen, R. J., Eskes, H., Flemming, J., Gaudel, A., Hendrick, F., Huijnen, V., Jones, L., Kapsomenakis, J., Katragkou, E., Keppens, A., Langerock, B., de Mazière, M., Melas, D., Parrington, M., Peuch, V. H., Razinger, M., Richter, A., Schultz, M. G., Suttie, M., Thouret, V., Vrekoussis, M., Wagner, A., and Zerefos, C.: Data assimilation of satellite retrieved ozone, carbon monoxide and nitrogen dioxide with ECMWF's Composition-IFS, Atmos. Chem. Phys., 15, 5275-5303, doi:10.5194/acp-15-5275-2015, 2015.
Inness, A., Baier, F., Benedetti, A., Bouarar, I., Chabrillat, S., Clark, H., Clerbaux, C., Coheur, P., Engelen, R. J., Errera, Q., Flemming, J., George, M., Granier, C., Hadji-Lazaro, J., Huijnen, V., Hurtmans, D., Jones, L., Kaiser, J. W., Kapsomenakis, J., Lefever, K., Leita ̃o, J., Razinger,M., Richter, A., Schultz, M. G., Simmons, A. J., Suttie, M., Stein, O., Th ́epaut, J.-N., Thouret, V., Vrekoussis, M., Zerefos, C., and the MACC team (2013). The MACC reanalysis: an 8 yr data set of atmospheric composition. Atmos. Chem. Phys., 13(8):4073–4109.
Inness, A., Benedetti, A., Flemming, J., Huijnen, V., Kaiser, J. W., Parrington, M., and Remy, S.: The ENSO signal in atmospheric composition fields: emission-driven versus dynamically induced changes, Atmos. Chem. Phys., 15, 9083-9097, doi:10.5194/acp-15-9083-2015, 2015.
Inness, A., Flemming, J., Suttie, M. and Jones, L., 2009: GEMS data assimilation system for chemically reactive gases. ECMWF RD Tech Memo 587. Available from http://www.ecmwf.int.
C. Ordonez, N. Elguindi, O. Stein, V. Huijnen, J. Flemming, A. Inness, H. Flentje, E. Katragkou, P. Moinat, V-H. Peuch, A. Segers, V. Thouret, G. Athier, M. van Weele, C. S. Zerefos, J-P. Cammas, and M. G. Schultz (2009): Global model simulations of air pollution during the 2003 European heat wave. Atmos. Chem. Phys., 10, 789-815, 2010. www.atmos-chem-phys.net/10/789/2010/
Stein, O., Flemming, J., Inness, A., Kaiser, J. W., and Schultz, M. G. (2012). Global re- active gases forecasts and reanalysis in the MACC project. Journal of Integrative Environmental Sciences, 1:1–14

## Slide 51: References: Areosols
Bellouin, N., J. Quaas, J.-J. Morcrette, and O. Boucher, 2013: Estimates of radiative forcing from the MACC re-analysis. Atmos. Chem. Phys., 13, 2045-2062.
Benedetti, A. et al, 2014: Operational dust prediction. Chapter 10 in: Knippertz, P.; Stuut, J.-B. (eds.), Mineral Dust – A Key Player in the Earth System, Springer Netherlands, 223–265, ISBN 978-94-017-8977-6. doi:10.1007/978-94-017-8978-3_10
Benedetti, A., Morcrette, J.-J., Boucher, O., Dethof, A., Engelen, R. J., Fisher, M., Flentje, H., Huneeus, N., Jones, L., Kaiser, J. W., Kinne, S., Manglold, A., Razinger, M., Simmons, A. J., and Suttie, M. (2009). Aerosol analysis and forecast in the European Centre for Medium-Range Weather Forecasts Integrated Forecast System: 2. Data assimilation. J. Geophys. Res., 114(D13):D13205
Benedetti, A., Kaiser, J. W., and Morcrette, J.-J. (2012). Global aerosols [in “State of the climate in 2011”]. Bull. Amer. Meteor. Soc., 93(7):S44–S46. (Also for subsequent years)
Huneeus, N., M. Schulz, Y. Balkanski, J. Griesfeller, S. Kinne, J. Prospero, S. Bauer, O. Boucher, M. Chin, F. Dentener, T. Diehl, R. Easter, D. Fillmore, S. Ghan, P. Ginoux, A. Grini, L. Horowitz, D. Koch, M.C. Krol, W. Landing, X. Liu, N. Mahowald, R. Miller, J.-J. Morcrette, G. Myhre, J. Penner, J. Perlwitz, P. Stier, T. Takemura, and C. Zender, 2011: Global dust model intercomparison in AEROCOM phase I. Atmos. Chem. Phys., 11, 7781-7816, doi:10.5194/acp-11-7781-2011.
Mangold, A., H. De Backer, B. De Paepe, S. Dewitte, I. Chiapello, Y. Derimian, M. Kacenelenbogen, J.-F. Léon, N. Huneeus, M. Schulz, D. Ceburnis, C. O'Dowd, H. Flentje, S. Kinne, A. Benedetti, J.-J. Morcrette, and O. Boucher, 2011: Aerosol analysis and forecast in the European Centre for Medium-Range Weather Forecasts Integrated Forecast System: 3. Evaluation by means of case studies, J. Geophys. Res.,116, D03302, doi: 10.1029 /2010JD014864.

## Slide 52: References: Areosols
Morcrette, J.-J., Boucher, O., Jones, L., Salmond, D., Bechtold, P., Beljaars, A., Benedetti, A., Bonet, A., Kaiser, J. W., Razinger, M., Schulz, M., Serrar, S., Simmons, A. J., Sofiev, M., Suttie, M., Tompkins, A. M., and Untch, A. (2009). Aerosol analysis and forecast in the European Centre for Medium-Range Weather Forecasts Integrated Forecast System: Forward modeling. J. Geophys. Res., 114(D6):D06206.
Morcrette, J.-J., O. Boucher, L. Jones, D. Salmond, P. Bechtold, A. Beljaars, A. Benedetti, A. Bonet, J.W. Kaiser, M. Razinger, M. Schulz, S. Serrar, A.J. Simmons, M. Sofiev, M. Suttie, A.M. Tompkins, A. Untch, and the GEMS-AER team, 2009: Aerosol analysis and forecast in the ECMWF Integrated Forecast System: Forward modelling. J. Geophys. Res., 114, D06206, doi: 10.1029 /2008JD011235.
Morcrette, J.-J., A. Beljaars, A. Benedetti, L. Jones, and O. Boucher, 2008: Sea-salt and dust aerosols in the ECMWF IFS. Geophys. Res. Lett., 35, L24813, doi:10.1029/2008GL036041.
Morcrette, J.-J., A. Benedetti, L. Jones, J.W. Kaiser, M. Razinger, and M. Suttie, 2011: Prognostic aerosols in the ECMWF IFS: MACC vs. GEMS aerosols. ECMWF Technical Memorandum, 659, 32 pp.
Morcrette, J.-J., A. Benedetti, A. Ghelli, J.W. Kaiser, and A.P. Tompkins, 2011: Aerosol-cloud-radiation interactions and their impact on ECMWF/MACC forecasts. ECMWF Technical Memorandum, 660, 35 pp.
Nabat, P., S. Somot, M. Mallet, I. Chiapello, J.-J. Morcrette, F. Solmon, S. Szopa, and F. Dulac, 2013: A 4-D climatology (1979-2009) of the monthly aerosol optical depth distribution over the Mediterranean and surrounding regions from a comparative evaluation and blending of remote sensing and model products. Atmos. Meas. Tech., 6, 1287-1314, doi:10.5194/amt-6-1287-2013.
Peubey, C., A. Benedetti, L. Jones, and J.-J. Morcrette, 2009: GEMS-Aerosol: Comparison and analysis with GlobAEROSOL data. In GlobAEROSOL User Report, October 2009, 11-20.

## Slide 53: References: Greenhouse Gases
A. Agusti-Panareda; S. Massart; F. Chevallier; G. Balsamo; S. Boussetta; E. Dutra; A. Beljaars
A biogenic C02 flux adjustment scheme for the mitigation of large-scale biases in global atmospheric CO2 analyses and forecasts. ECMWF Technical Memorandum, no 773, 2015
http://www.ecmwf.int/en/elibrary/technical-memoranda
Agusti-Panareda, A., S.Massart, F.Chevallier,S.Boussetta, G.Balsamo, A.Beljaars, P.Ciais, N.M.Deutscher, R.Engelen, L.Jones and R.Kivi, J.-D.~Paris, V.-H. Peuch, V.Sherlock, A.T.Vermeulen, P.O.Wennberg, D.Wunch, 2014: Forecasting global atmospheric CO2, Atmospheric Chemistry and Physics ,14, 11959-11983, doi:10.5194/acp-14-11959-2014
Chevallier, F., R. J. Engelen, C. Carouge, T. J. Conway, P. Peylin, C. Pickett-Heaps, M. Ramonet, P. J. Rayner, and I. Xueref-Remy, 2009. AIRS-based vs. flask-based estimation of carbon surface fluxes. J. Geophys. Res., 114, D20303, doi:10.1029/2009JD012311.
Chevallier, F., R. J. Engelen, and P. Peylin, 2005. The contribution of AIRS data to the estimation of CO2 sources and sinks. Geophys. Res. Lett., 32, L23801, doi:10.1029/2005GL024229.

## Slide 54: References: Greenhouse Gases
Engelen, R.J., S. Serrar, and F. Chevallier, 2009. Four-dimensional data assimilation of atmospheric CO2 using AIRS observations. J. Geophys. Res., 114, D03303, doi:10.1029/2008JD010739.
Engelen, R.J. and A. P. McNally, 2005. Estimating atmospheric CO2 from advanced infrared satellite radiances within an operational four-dimensional variational (4D-Var) data assimilation system: Results and validation. J. Geophys. Res., 110, D18305, doi:10.1029/2005JD005982
Massart et al. (2016)
Ability of the 4-D-Var analysis of the GOSAT BESD XCO2 retrievals to characterize atmospheric CO2 at large and synoptic scales. Atmos. Chem. Phys., 16, 1653–1671, www.atmos-chem-phys.net/16/1653/2016/
doi:10.5194/acp-16-1653-2016. http://www.atmos-chem-phys.net/16/1653/2016/acp-16-1653-2016.pdf
Massart, S. and Agusti-Panareda, A. and Aben, I. and Butz, A. and Chevallier, F. and Crevoisier, C. and Engelen, R. and Frankenberg, C. and Hasekamp, O., 2014: Assimilation of atmospheric methane products in the MACC-II system: from SCIAMACHY to TANSO and IASI0, Atmospheric Chemistry and Physics, 14, 6139–6158,10.5194/acp-14-6139-2014.

## Slide 55: References: General
Granier, C., Bessagnet, B., Bond, T., D’Angiola, A., Dernier van der Gon, H., Frost, G., Heil, A., Kaiser, J., Kinne, S., Klimont, G., Kloster, S., Lamarque, J.-F., Liousse, C., Masui, T., Meleux, F., Mieville, A., Ohara, T., Raut, J.-C., Riahi, K., Schultz, M., Smith, S., Thompson, A., van Aardenne, J., van der Werf, G., and van Vuuren, D. (2011). Evolution of anthropogenic and biomass burning emissions of air pollutants at global and regional scales during the 1980–2010 period. Climatic Change, 109(1-2):163–190.
Hollingsworth, A., Engelen, R. J., Textor, C., Benedetti, A., Boucher, O., Chevallier, F., Dethof, A., Elbern, H., Eskes, H., Flemming, J., Granier, C., Kaiser, J. W., Morcrette, J.-J., Rayner, P., Peuch, V.-H., Rouil, L., Schultz, M. G., and Simmons, A. J. (2008). Toward a monitor- ing and forecasting system for atmospheric composition: The GEMS project. Bull. Amer. Meteor. Soc., 89(8):1147–1164.
References: Fires
Kaiser, J. W., Heil, A., Andreae, M. O., Benedetti, A., Chubarova, N., Jones, L., Morcrette, J.-J., Razinger, M., Schultz, M. G., Suttie, M., and van der Werf, G. R. (2012). Biomass burning emissions estimated with a global fire assimilation system based on observed fire radiative power. Biogeosciences, 9:527–554.
Kaiser, J. W. and van der Werf, G. R. (2012). Global Biomass Burning [in ”State of the Climate in 2011”]. Bull. Amer. Meteor. Soc., 93(7):S54–S55. (also for other years)
Kaiser, J.W., M. Suttie, J. Flemming, J.-J. Morcrette, O. Boucher, and M.G. Schultz, 2009: Global real-time fire emission estimates based on space-borne fire radiative power observations. AIP Conf. Proc., 1100, 645-648.