## Slide 1
Flood Forecasting
Fredrik Wetterhall (fredrik.wetterhall@ecmwf.int)
European Centre for Medium-Range Weather Forecasts

## Slide 2: Hydrology – modelling the water cycle on land
Notes: The hydrological cycle

## Slide 3: Operational flood forecasting chain
EPS
Hydrological model
Flood warning
Preprocessing/
calibration
Post-processing
Notes: The forecasting chain consists of input meteorological forecasts who are pre-processed and then run through a hydrological model that produces discharge. The probabilistic information is summarised in warning tables and a flood warning is issued if a threshold is exceeded.

## Slide 4: The European Flood Awareness System (EFAS)
Early probabilistic flood warnings across Europe
Transboundary
50 partners
Partners provide:
Observations
Feedback on warning performance
Development of decisions
EFAS has the largest collection of hydro-meteorological observations in Europe!

## Slide 5: How do we actually do flooding prediction? Schematic view
Expert Knowledge of
Member States
Real-time data
(EU-FLOOD-GIS/ETN-R)
Europ. Data Layers
Meteo – Data / forecasts
Historical Data
Static Data
EFAS partner network
Alert email
EFAS user interface
DATA
Hydrological modeling
Linz, AT – 31/05/2013 00 UTC

## Slide 6: Flood warning for Passau, Germany 30 May 2013
Donau at Passau (DE), 30/5/2013
Although the flood was predicted it was not high enough. Top discharge should have been 10000
Notes: The image shows the EFAS multi-model streamflow prediction for Passau, Germany. Forecast date is 30/05/2013 12 UTC. The colours indicate the different alert levels.
The box plots show the ECMWF ENS, the red line the ECMWF Highres, the black line the DWD COSMO.
The forecasts gives a clear indication of a flooding in 4-5 days

## Slide 7: Additional point information
Upstream precipitation
Upstream snowmelt
Average temperature
Overview of threshold exceedances
Persistence diagram
COSMO-LEPS ESP

## Slide 8: Play the game!