## Slide 1
Giovanna De Chiara
Satellite information on the ocean surface: Scatterometer and Altimeter
15 March 2016
with contributions from Saleh Abdalla, Magdalena Balmaseda, Hao Zou, Patrick Laloyaux

## Slide 2
Scatterometer Winds
The importance of scatterometer wind observations
Scatterometer principles
Data usage at ECMWF and their impact
How we can improve usage and impact
Altimeter Wind, Waves, Sea Surface Height
Altimeter principles
Use of altimeter data in the wave and ocean models
Altimeter data impacts
Outline

## Slide 3
Why is Scatterometer important?
The scatterometer measures the ocean surface winds (ocean wind vector).
Ocean surface winds:
affect the full range of ocean movement
modulate air-sea exchanges of heat, momentum, gases, and particulates
direct impact on human activities
Wind observations below 850 hPa
FSO values relative quantities (in %)
Wide daily coverage of ocean surface winds
[Horanyi et al., 2013]
Ex: 1 day of ASCAT-A data

## Slide 4
A Scatterometer is an active microwave instrument (side-looking radar)
  Day and night acquisition
  Not affected by clouds
The return signal, backscatter (σ0 sigma-nought), is sensitive to:
  Surface wind (ocean)
  Soil moisture (land)
  Ice age (ice)
Scatterometer
Scatterometer was originally designed to measure ocean wind vectors:
  Measurements sensitive to the ocean-surface roughness due to capillary gravity waves generated by local wind conditions (surface stress)
  Observations from different look angles: wind direction
Returned
Incoming

## Slide 5: Scatterometer
The amount of backscatter depends on:
The frequency and polarization of the emitted wave
Backscatter highly depends on:
Wind speed
Relative direction between the surface wind and look angle
  Incidence angle
C-band (5.3 GHz): λ ~ 5.6 cm
Ku-band (14.6 GHz): λ ~ 2.1 cm
Bragg scattering occurs from the ocean capillary-gravity waves (cm-range) that are in resonance with the microwaves

## Slide 6
Dependency of the backscatter on... Wind speed

## Slide 7
upwind
downwind
crosswind
Dependency of the backscatter on... Wind direction
upwind
downwind
Wind direction wrt Beam
  Asymmetry Upwind – Downwind (particularly small)
  Asymmetry Upwind – Crosswind

## Slide 8
Dependency of the backscatter on... Wind direction
Backscatter response depends on the relative angle between the pulse and capillary wave direction (wind direction)
Fore Beam
Mid Beam
Aft Beam
Wind direction wrt Mid Beam
Wind direction wrt Mid Beam
Wind direction wrt Mid Beam
Mid
Fore
Aft
C-band SCAT geometry

## Slide 9
How can we relate backscatter to wind speed and direction?
The relationship is determined empirically
Ideally collocate with surface stress observations
In practice with buoy and 10m model winds
Geophysical model functions (GMF) families
C-band: CMOD (currently CMOD5.N)
Ku-band: NSCAT, QSCAT
U10N: equivalent neutral wind speed
: wind direction w.r.t. beam pointing
: incidence angle
p : radar beam polarization
: microwave wavelength

## Slide 10
How can we relate backscatter to wind speed and direction?
For the C-band data, σ0 triplets lies on a double conical surface
σ0 triplets with the same wind speed
Wind inversion: search for minimum distances between the σ0 triplets and all the solutions on the GMF surface.
Noise in the observations can change the position wrt the cone: wind direction ambiguities
0°
90°
180°
270°
CMOD5
z_aft
z_fore
z_mid
[Stoffelen]
0 ° or 180 °???

## Slide 11
C- band scatterometers
Used on European platforms (1991 onwards):
SCAT on ERS-1, ERS-2 by ESA
ASCAT on Metop-A, Metop-B by EUMETSAT
f~5.3 GHz (λ~5.7 cm)
VV polarization
Three antennae
Pros and cons:
Hardly affected by rain
High quality wind direction (especially ASCAT)
Two nearly opposite wind solutions
Rather narrow swath:
ERS-1/2: 500km
ASCAT-A/B: 2x550km

## Slide 12
Ku-band scatterometers
Used on US, Japanese, Indian and Chinese platforms:
NSCAT, QuikSCAT, SeaWinds by NASA (and Japan)
Oceansat by ISRO
Haiyang-2A by China
RapidSCAT on the ISS
Pros and cons:
Up to four wind solutions (rank-1 most often the correct one)
Broad swath (1,800km)
Affected by rain
Problems regarding wind direction:
  azimuth diversity not good in centre of swath
  outer 200km only sensed by one beam.
f~13 GHz (λ ~ 2.2 cm)
VV and HH polarization:
Two rotating pencil-beams (4 look angles)
OSCAT daily coverage

## Slide 13
Operational usage of scatterometer winds at ECMWF
95 | 96 | 97 | 98 | 99 | 00 | 01 | 02 | 03 | 04 | 05 | 06 | 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16
ERS-1
ERS-2
ERS-2 (Regional Mission Scenario)
QuikSCAT
METOP-A ASCAT
METOP-B ASCAT
Oceansat-2 (OSCAT)
C-Band
Ku Band
(RapidSCAT)
Under Monitoring

## Slide 14
Scatterometer assimilation strategy
 | C-band | Ku-Band
Resolution | 25 km | 50 km
σ0 bias correction | √ | -
Wind Inversion | ECMWF | KNMI
Wind Speed bias correction | √ | √
QC – Sea Ice check | √ | √
Rain flag check | - | √
Thinning | 100 km | -
Maximum wind speed assimilated | 35 m/s | 25 m/s
Assigned observation error | 1.5 m/s | 2 m/s
4D-Var | 2 solutions | 1 solution
Assimilated as 10m eq. neutral wind (U&V) | √ | √

## Slide 15
C-band: Ambiguous vector wind (U&V) - wind selection based on background winds
Purely quadratic cost function
For SCATT, 10m equivalent neutral wind (ENW), rather than 10m wind are used to take into account for stability effects:
  for stable atmospheric stratification ENW is smaller than wind
  for unstable atmospheric stratification ENW is larger than wind
on average the difference is 0.2 m/s
Scatterometer assimilation strategy

## Slide 16: ASCAT-A wind data

## Slide 17
TC Haiyan – CY40R1 2013110712 [Assimilation Window 9 - 21]
1 ASCAT-A obs @ 1pm
Philippines
Is the model able to vertically propagate the information?
Single observation experiments

## Slide 18
00 [09h]
03 [12h]
06 [15h]
09 [18h]
12 [21h]
T1279
Single Observation Experiments (1 ASCAT-A)

## Slide 19
U An Incr @ 18h
U An Incr @ 18h
ML 114
V An Incr @ 18h
Model Levels
137
100
50
ML PL(hPa)
137 ~ 1013
114 ~ 850
96 ~ 500
79 ~ 250
60 ~ 100
137
100
50
N
S
N
Res ~ 16 km
S
Single Observation Experiments (1 ASCAT-A)

## Slide 20: Impact of scatterometer winds
Contribution to the reduction of the 24h Forecast Error (total dry energy norm) [Cardinali, 2009]
Global statistics with respect to the total observing network Dec 2012 / Feb 2013

## Slide 21
For each storm the min SLP have been detected from the ECMWF model fields
SLP have been compared to observation values (from NHC and JMA)
Statistics based only on cases where ASCAT-A, ASCAT-B and OSCAT passes were available
Dec 2012/ Feb 2013
Impact of scatterometer winds on Tropical Cyclone FC

## Slide 22
Verified against conventional temperature observations
[P. Laloyaux]
Tropical Atlantic
Tropical Indian
Tropical East Pacific
Temperature difference Scatt – NoScatt
November 2013
Impact of scatterometer winds …on the ocean parameters

## Slide 23
How can we improve usage and impact?
Include dependency from other geophysical quantities such as ocean currents
Stress is related to relative wind
The observation operator should act on relative wind
Accurate ocean current input are needed
10m ASCAT-A wind speed
10m FG wind speed
Improve QC mostly for extreme events
  Because of thinning and QC the strongest winds can be rejected
Test on the observation error, thinning and use of high resolution products
TC Haiyan

## Slide 24
CTRL
VarQC/Thin=4/ObsErr=1.5m/s
HN
VarQC / Thin=2
HN & Thin=2
HN & Thin=2 & Obserr=0.5
TC QC issues
TC KILO – 2015090812

## Slide 25: Scatterometer Concluding remarks
ECMWF has a long experience with scatterometry
Available continuously from 1991 onwards:
GMF development
Monitoring, validation, assimilation, re-calibration
On-going efforts to improve usage and impact
Improve QC
Adapt observation errors, thinning, super-obbing
Include dependency from other geophysical quantities
Use in the Reanalysis
ERS1/2 and QuikSCAT in ERA-Interim
ASCAT-A reprocessed products used in ERA5
Scatterometer observations widely used in NWP
Ocean wind vectors
Positive impact on analysis and the forecast
Global scale and extreme events
Impact on Atmospheric, Ocean and Wave model
Typhoon Haiyan 20131107
ASCAT-A ASCAT-B OSCAT

## Slide 26: Radar Altimeters
Radar altimeter is a nadir looking instrument.
Specular reflection.
Electromagnetic wave bands used in altimeters:
Primary:
Ku-band (~ 2.5 cm) – ERS-1/2, Envisat, Jason-1/2/3, Sentinel-3
Ka-band (~ 0.8 cm) – SARAL/AltiKa (only example)
Secondary:
C-band (~ 5.5 cm) – Jason-1/2/3, Topex, Sentinel-3
S-band (~ 9.0 cm) – Envisat
Sentinel-3
Radar Altimeter (SRAL)
Envisat 1-day coverage
Main parameters measured by an altimeter:
  Sea surface height (ocean model)
  Significant wave height (wave model)
  Wind speed (used for verification)

## Slide 27: How Altimeter Works
surface
Height=∆t/2  c
emitted signal returned signal
a t m o s p h e r e
time
ocean surface
illuminated area
Power of illumination
radar signal
time
power
flat surface
rough surface

## Slide 28: Sea Surface Height
Time delay  sea surface height
  Radar signal attenuation due to the atmosphere is caused by:
    Water vapour impact: ~ 10’s cm.
    Dry air impact: ~ 2.0 m
    Correction made using radiometer and model data
time
power
waveform

## Slide 29: Surface wind speed
  Backscatter is related to water surface Mean Square Slope (MSS)
  MSS can be related to wind speed
  Stronger wind  higher MSS  smaller backscatter
  Errors are mainly due to algorithm assumptions, waveform retracking (algorithm), unaccounted-for attenuation & backscatter.
amplitude of returned signal  wind speed
time
power
waveform
emitted signal backscatter

## Slide 30: Significant Wave Height (SWH)
time
power
waveform
slope of leading edge  SWH
  SWH is the mean height of highest 1/3 of the surface ocean waves
  Higher SWH  smaller slope of waveform leading edge
  Errors are mainly due to waveform retracking (algorithm) and instrument characterisation.

## Slide 31: Operational Assimilation of SWH (wave model)
Assimilation method for SWH data:
  Data are subjected to a quality control process (inc. super-obbing).
  Bias correction is applied.
  Simple optimum interpolation (OI) scheme on SWH.
  The SWH analysis increments  wave spectrum adjustments…
10 Mar. 2009
Jason-1 Envisat
Jason-2 Envisat
Envisat
8 Jun. 2009
Jason-1 Jason-2 Envisat
1 Apr. 2010
Jason-2 Envisat
7 Apr. 2012
Jason-2
22 Oct. 2003
ERS-2
1 May 1996
ERS-1
15 Aug. 1993
1 Feb. 2006
12 May 2015
Jason-2 Cryosat-2 SARAL
Jason-3 OGDR (~Q2, 2017); Sentinel-3 (~Q2, 2017).

## Slide 32: Impact of one additional altimeter on the SWH analysis [CS & J2] - [J2 only]
Impact of SWH assimilation

## Slide 33
Altimeter data in the Ocean Model
10cm
30 m
From sea level observation it is possible to infer information on the vertical density structure
SLA = Sea Level Anomaly
Assimilated in the ocean model
SLA
The altimeter measures the range which can used to determine Sea Surface Height (SSH)
SSH

## Slide 34
El Nino 2015/2016
SL Anomalies Feb 2016
Lon/Depth Temp anom Feb 2016

## Slide 35
Sea surface height observations from satellite (i.e. AVISO L3 along track SLA data) are assimilated in ECMWF ocean reanalysis (ORAS4, ORAP5 and ORAS5) system using NEMOVAR.
Satellite data includes observations from ERS-1/2, Envisat, Jason-1/2 and Topex/Poseidon (In the future also AltiKa, HY-2A).
The SLA along track data has very high spatial resolution for the 1 degree “class” of ocean assimilation systems  Features in the data which the model can not represent. This can be dealt with in different ways:
  Inflate the observation error to account for non representativeness of the “real” world in the assimilation system
  Construction of “superobs” by averaging
  Thinning
Operational Assimilation of SLA
Obs SLA 10 days
Model (1 deg) SLA in 10 days

## Slide 36
superob
thinning
raw
super-observation is created by averaging SLA value, space/time positions
Thinning is randomly select one observation within each superob-grid
share the same obs number, superob grid and OBE
evaluate with 5 ensemble member in ¼ degree reanalysis for 5 yrs
Operational Assimilation of SLA
Before the assimilation, a thinning or superobbing scheme is normally implemented to avoid over sampling of the satellite observations.

## Slide 37: Impact of assimilating altimeter SLA: Time correlation with altimeter SL product
CNTL
NEMOVAR TS
ORAS4 (TS+Alti)
Impact of SLA assimilation

## Slide 38: Altimeter Concluding remarks
ECMWF has a long experience with altimetry in the wave model
Available continuously from 1993 onwards:
ERS1/2, Envisat, Jason1/2, Cryosat, Saral…
  Future missions: Jason-3, Sentinel-3,…
  Altimeter wind and wave data are used for:
  Data assimilation
  Error estimation
  Use in reanalyses (assimilation and validation)
  Long term assessments & climate studies
  Monitoring of model performance (inc. model resolution) & Assessment of model changes
  Altimeter sea level anomaly:
  Use for assimilation and validation
  Significant impact for surface and sub-surface ocean
  Importance for reanalysis and climate studies
  Uncertainty from the ensemble members potentially used for model error