## Slide 1: Microwave observations in clear-sky conditions
Alan Geer
Thanks to: Bill Bell, Peter Bauer

## Slide 2: Overview
General introduction to the microwave (today)
  The microwave spectrum
  Microwave instruments
Clear-sky microwave (today)
  Imager channels and the surface, water vapour and temperature sounding
  Practical use of AMSU-A channel 5 at ECMWF
All-sky microwave (Wednesday)
  Interaction of particles with microwave radiation
  Solving the scattering radiative transfer equation
  Cloud screening for clear-sky assimilation
  All-sky assimilation

## Slide 3: FSOI of satellite radiances, August 2016 100% = full operational observing system
Microwave WV 20.4%
Microwave T 20.1%
Infrared T 16.5%
Infrared WV 5.4%
Microwave instruments together account for 40% of forecast impact, with “moist” assimilation (WV, cloud, precipitation channels) having nearly as much impact as “dry” assimilation (T channels)

## Slide 4: General introduction to the microwave

## Slide 5
Visible
SEVIRI channel 1
0.56-0.71 μm
Microwave
AMSR-E channel 37v
8108 μm (37 GHz v-pol)
TB [K]
Window channels
24th August 2008 at around 12UTC
Infrared
SEVIRI channel 10
11-13 μm
from Dundee Satellite Receiving Station, © Eumetsat

## Slide 6: Where is the microwave?
Planck function
Solar
T = 6000K
Terrestrial
T = 290K
Normalised radiance
Frequency
Wavelength
10m
10cm
1mm
10μm
0.1μm
Microwave
Radio
Infrared
Ultraviolet
Visible

## Slide 7: How much energy is there?
Solar
T = 6000K
Terrestrial
T = 290K
Planck
Function
Radiance
W m-2 sr-1 Hz-1
Flux
W m-2 Hz-1
Terrestrial
radiance × 6.28 sr
Solar
radiance × 6×10-5 sr
Deep space
T = 2.7K
Deep space
radiance × 6.28 sr
Flux
10-12 W m-2 Hz-1
Frequency [103 THz]
Solar
Terrestrial

## Slide 8: Brightness temperature (TB)
Radiance that would be produced by black-body radiation of a specified temperature TB (Planck function)
In the microwave, we can use Rayleigh-Jeans approximation:
Convert radiance (a non-intuitive quantity) into the “radiant temperature”
Radiance
Brightness temperature

## Slide 9
H2O Rotation lines
+
Water vapour continuum
O2 Rotation Lines
+
Dry air continuum
The microwave spectrum
Absorption coefficientβa [1/km]
Moist
Dry
Moisture sounding:
22 GHz and 183 GHz water vapour lines
Temperature sounding:
60 GHz oxygen line
“Imaging channels” in the windows

## Slide 10: AMSU: cross track microwave sounder
Aperture: D< 30cm
Purpose: temperature and moisture sounding
AMSU A1
AMSU A2
AMSU B
Channels 3-15
(50-57 GHz, 89 GHz)
Channels 1&2
(23.8 GHz, 31.4 GHz)
Channels 15-20
(89, 150, 3 × 183GHz)

## Slide 11: SSMIS – A conical microwave sounder / imager
60 cm

## Slide 12: GMI: imager, targeting preciptiation
NOAA
NASA / JAXA
Global precipitation mission:
Launched Feb 2014
Precipitation radar at 13 GHz and 36 GHz

## Slide 13: Field of view size and aperture approximate calculations in a diffraction-limited system
Airy disk size:
θ
Wavelength
D
a
Aperture size
Satellite to earth distance
FOV size
x
T-sounder: 50 GHz: λ ≈ 0.006 m
(like AMSU-A) satellite altitude 800 km
aperture 0.3 m
FOV ≈ 40 km
Imager: 20 GHz: λ ≈ 0.016 m
(like GMI) satellite altitude 400 km
45° view angle: a=600 km
aperture 1.2 m
FOV ≈ 20 km

## Slide 14: Active microwave: radar
NOAA
NASA / JAXA
Global precipitation mission:
Launched Feb 2014
Precipitation radar at 13 GHz and 36 GHz

## Slide 15: Frequency allocation and protection
3 KHz
30 GHz
300 GHz
Earth observation
Sky Sports

## Slide 16: Clear-sky observations: earth surface, atmospheric water vapour and temperature

## Slide 17
H2O Rotation lines
+
Water vapour continuum
O2 Rotation Lines
+
Dry air continuum
The microwave spectrum: window channels
Absorption coefficientβa [1/km]
Moist
Dry
“Imaging channels” in the windows

## Slide 18: Observations at 10 GHz v-polarisation from AMSR-E, 55° zenith angle
TB [K]
Ocean TB | ≈ 170 K | ≈ -100°C
Land TB | ≈ 280 K | ≈ 10°C
Sea ice and Antarctica TB | ≈ 240 K | ≈ -30°C

## Slide 19: Radiation and the earth’s surface
Emission
Direct reflection
Emissivity

## Slide 20
TB [K]
Observed, 10 GHz, v-pol
Surface emissivity
Estimated, 10 GHz, v-pol

## Slide 21: Sea surface emissivity depends on wind speed
Surface emissivity
Modelled, 10 GHz, v-pol
10m wind speed
First guess [ms-1]

## Slide 22: Emissivity physics: oceans
Plane water surface: low emissivity - Fresnel equations
Macro structure: waves, swell – geometric optics
Micro structure, e.g. cm: diffraction from capillary waves
Foam: much higher emissivity than water
Correction for non-specular reflection
NOAA Ocean Explorer

## Slide 23: Ocean surface emission is polarised
TB [K]
10 GHz v-pol
TB [K]
10 GHz h-pol
Ocean TB:
~150 K v-pol
~90 K h-pol

## Slide 24: Land surface emission
Emissivity is highly variable in time and space:
  Vegetation cover
  Surface roughness and composition: sand, rock, earth
  Soil moisture
  Presence of open water or snow
Surface temperature is also hard to deal with:
  Varies significantly from day to night
  Radiating “skin temperature” is hard to define
    May vary with frequency
    Radiation might come from some distance below the surface in the case of sand desert
Practical solution: emissivity retrievals or emissivity atlases

## Slide 25: Window channels: summary
Surface emissivity is the most important radiative effect:
  Land surfaces ~ 0.9
    Moisture, vegetation, surface characteristics
  Ocean surfaces ~ 0.3 – 0.6
    Polarised
    Dependent on sea-state (wind and wave)
NWP information content:
  Oceans:
    Column water vapour, cloud/precipitation, wind speed
  Land:
    Retrieving emissivity for use with sounding channels
    (Soil moisture)
  Cloud and precipitation (tomorrow)

## Slide 26
H2O Rotation lines
+
Water vapour continuum
O2 Rotation Lines
+
Dry air continuum
The microwave spectrum: water vapour channels
Absorption coefficientβa [1/km]
Moist
Dry
Moisture sounding:
183 GHz water vapour line

## Slide 27: SSMIS F-17 183+/-1 GHz
Observed TB [K]
High RH
Low RH
Convection

## Slide 28: Humidity-sounding weighting functions
High humidity: weighting function high in troposphere
Low humidity: weighting function lower in troposphere
TB = 230 K (found at approx. 400 hPa)
TB = 265 K (found at approx. 700 hPa)

## Slide 29
H2O Rotation lines
+
Water vapour continuum
O2 Rotation Lines
+
Dry air continuum
The microwave spectrum: temperature channels
Absorption coefficientβa [1/km]
Moist
Dry
Temperature sounding:
60 GHz oxygen line

## Slide 30
53.6 GHz
SSMIS channel 3: like AMSU-A channel 5, but with a fixed zenith angle
TB [K]
Midlatitude Rossby waves
Deep convection
High mountains

## Slide 31: Fine-scale structure in the 60 GHz oxygen line
Level to TOA transmittance
from Liebe MPM 92 model
Narrow lines ~ several MHz
Increasing pressure
broadening
Typical MW radiometer passband
at 54.4 GHz

## Slide 32: AMSU-A 50-60 GHz temperature channels
Channel positions and bandwidths are based on trade-offs aimed at simultaneously optimising :
  width of the band (wider bands give lower noise)
  flatness of optical depth across the band (narrow weighting functions)

## Slide 33: AMSU-A clear-sky nadir weighting functions these are approximately fixed, unlike humidity weighting functions
7 0%
6 0%
5 5%
4 19%
3 56%
2 92%
Channel
Transmittance to space

## Slide 34: Use of AMSU-A channel 5 at ECMWF

## Slide 35: AMSU-A channel 5 radiances: Metop-A satellite, 9pm 25/4 to 9am 26/4/2012
Observed TB [K]
First guess TB [K]
“Clear sky” assumption: no cloud or precipitation radiative transfer

## Slide 36: AMSU-A channel 5 radiances
First guess departures [K]
Scan bias
General “warm” bias

## Slide 37: AMSU-A channel 5 radiances
Bias correction [K]
Airmass correction (layer mean temperature)
Scan bias correction
Mean offset

## Slide 38: AMSU-A channel 5 radiances
Bias corrected first guess departures [K]
Still some scan bias
Precipitation and cloud
The Andes
Sea ice
Snow and ice

## Slide 39: AMSU-A channel 5 radiances
Bias corrected first guess departures [K]
Still some scan bias
Precipitation and cloud
The Andes
Sea ice
Snow and ice
After blacklisting

## Slide 40: AMSU-A channel 5 radiances
Bias corrected first guess departures [K]
After blacklisting

## Slide 41: AMSU-A channel 5 radiances
Bias corrected first guess departures [K]
After blacklisting
After active thinning and VarQC

## Slide 42: AMSU-A channel 5 radiances
Bias corrected first guess departures [K]
After blacklisting
After active thinning and VarQC

## Slide 43: AMSU-A channel 5 radiances
Departures normalised by
observation error, σo = 0.28K
(Absolute values < 0.5 removed here for visual clarity)

## Slide 44: AMSU-A channel 5 radiances
Contribution to cost function (as before, low contribution values removed for clarity)

## Slide 45: Now we need to minimise 4D-Var
Health warning - there are a few notational shortcuts and simplifications here… please don’t build an assimilation system based on this slide.
and its gradient
Feed the minimisation algorithm with…
Cost function
What we just calculated
The TL and adjoint version of the radiative transfer
…and it spits out the analysis:

## Slide 46: What did 4D-Var do with AMSU-A channel 5, and all the other observations in the analysis?
Increment [K]
FG departure [K]
1:1 line - if the analysis exactly fitted the observations
Just a little nudge in the direction of the observations

## Slide 47: Summary: clear-sky microwave
“Imaging” (window) channels:
  In window regions and less-intense lines, e.g. 22 GHz water vapour line
  Sensitive to skin temperature, wind speed, sea ice, column water vapour
Water vapour sounding channels:
  183 GHz water vapour line
  Sensitive to broad-layer tropospheric humidity
Temperature sounding channels:
  60 GHz oxygen line
  Sensitive to broad-layer temperature, with multiple channels to cover from troposphere to stratosphere